## Slide 1: Machine Safety and Logic
November 5, 2015

## Slide 2: Objectives
  Read Section 8.23.4 To 8.23.8 Section of DX200 updated manual
  Review Machine Safety Hardware
  Expansion function
  Response Time
  Safety Logic Circuit
  I/O configuration
  Offline Programming
  Standards applications

## Slide 3: Hardware
  Standard in all DX200 Controllers
  Breakout card (YCF22)
    CN219 on schematics
  Machine I/O board (YSF22B-E)
  Machine Safety board (YSF21-E)

## Slide 4: Hardware
Sheet 5 of schematics
Servo OnEnable 1-4
Ext Axis Overrun 1-3
STO
(Independent Control)
Non standard setup

## Slide 5: Hardware
Sheet 5A of schematics
Servo Direct Inputs 1-6 (Rapid inputs)
AXIN 1 &2
AXOUT 1 &2
Full Speed Test
Slow Speed Mode

## Slide 6: Hardware
Sheet 5B of schematics
External Enable
  (Deadman)
Machine Safety Inputs (GSIN1 &2)
Machine Safety Outputs (GSOUT1 &2)
Machine Safety EDM (GSEDM1 &2)
STO Function
Note: EDM Jumpers not installed on Standard
Safety I/O
2 Inputs (Dual Channel)
  Sink/Source
2 Outputs (Dual Channel)
  Sink/Source

## Slide 7: Expansion function
  Adds communication between machine safety and functional safety (FSU)

## Slide 8: Expansion function
  Option Function for software 1.8 and greater
  Must be in yaskawa mode to enable
  Use safety boards that are in safety logic circuit.

## Slide 9: Safety Logic Circuit
128 Lines of Logic
4 ms scan time
2 input signals 1 output signal per line – basic.
Backup File YSFLOGIC.DAT

## Slide 10: 1. Logic

## Slide 11: 2. Input Signals

## Slide 12: 2. Input Signals

## Slide 13: 3. Output Signals
#n FSB OUT Functional Safety Output 8 points

## Slide 14: 4. Timer
Select off or on delay

## Slide 15: Expansion function
Program must be written and confirmed.
  After modification
  After loading YSFLOGIC.DAT file from network
  Loading CMOS

## Slide 16: I/O Configuration
  SLC signal display setup
  Assignment of functional safety output signals
  Assignment of ext output signals

## Slide 17: SLC signal display setup
Standards set all signals but PPDSM to Normal Close
Write and Confirm to change setting on pendant
Setup is located YSFLOGIC.DAT file of robot.

## Slide 18: F Safety Signal Allocation - Output Signals
The FSU hardware outputs (FSBOUT) can be assigned for use in machine safety logic.
  Assignment of a FSBOUT set to YSF21-E, the output can only be used by machine safety logic
  Assignment of a FSBOUT set to YSF25-E #n output can be used by FSU functions only
  Setting of not used can’t be used by machine safety logic or FSU functions.
  Use page key to configure multiple FSU configurations
  Use of older standard may need to add this configuration.

## Slide 19: SLC EXT signal allocation
The FSU logical outputs (FSOUT)can be assigned for use in multiple FSU units.
  Assignment of a FSOUT set to YSF25-E #n, the output can only be used by the n FSU functions.
    For example, YSF25-E #2 is available for use for FSU in R2 functions
  Setting of not used can’t be used by any robot’s FSU.

## Slide 20: Safety Logic Circuit Comments
32 Characters
Press main menu if you can’t see comments. Cursor to right side.
Font size can be changed under the display settings icon
Must write and confirm comments

## Slide 21: Troubleshooting
  Check I/O Status
  Check Logic Status
Input signals are filled when off, and outlined when on
Logic filled when on, outlined when off

## Slide 22: CIO Signals
  Safety Fieldbus (Inputs 1-64,Outputs 1-64)
  FSB (Boards 1- 8, Inputs 1-8, Output 1-8)
  Safety Logic Circuit (MS Out 1-64)
  Funtional Safety logic circuit (FS Out 1-64)
  How can these CIO signals effect the electrical design?

## Slide 23: Example
  Add manual E-Stop reset
  Hardware
    Add Dual channel reset to functional safety input 2.
    Add E-Stop reset lamp to universal output 24.
  Draw logic on paper in robot format
    MSOUT 21 used instead of R24 for CIO address to write logic for reset lamp.
    MSOUT 21 is CIO address 81344

## Slide 24: Example
How could E-Stop OK Output be programmed to #1 FSB Output 2?
Set SLC display setup for FSBIN to normally closed.

## Slide 25: DX200 ArcWorld IV 6X00 with integrated safety logic
Information located under Standard World Jobs
Removed Pilz Multi safety PLC
Theory of operation document explains safety operation, FSU files setup, and safety logic
Side A/B switches are no longer used on positioner
  May be physically on positioner
  FSU Axis range limit function used
Integrated safety logic uses status from FSU to solve logic and perform safety function.
  Reduces wiring and external hardware
FSU standard only on R1
SYS Critical FSU Funct Disabled alarm
Safety checkout of system uses QC check sheet

## Slide 26: DX200 ArcWorld IV 6X00 with integrated safety logic
SLC Signal Display Setup

## Slide 27: DX200 ArcWorld IV 6X00 with integrated safety logic
F-Safety Signal Allocation
SLC EXT Signal Allocation

## Slide 28: DX200 ArcWorld IV 6X00 with integrated safety logic
  Inputs for integrated safety logic
  #1 FSU In1 – Light Curtain (hardwired)
  FSU files- Positioner At side A/B
Why is light curtain relay used?

## Slide 29: DX200 ArcWorld IV 6X00 with integrated safety logic

## Slide 30: DX200 ArcWorld IV 6X00 with integrated safety logic
  Break down safety logic to specfic safety functions
  S1 Standstill – Stops motion of positoner trunion
  S2 Standstill – Stops motion of Side A tool
  S3 Standstill – Stops motion of side B Tool
  S2 Speed limit – Limits Side A speed to 30%
    Safety distance requirement
  S3 Speed limit – Limits Side B speed to 30%
    Safety disatnce requirement
  Servo Off Cat1 – Stops motion of robot(s) and postioner Trunion and tooling axis

## Slide 31: DX200 ArcWorld IV 6X00 with integrated safety logic
S1 Standstill Positioner Trunion – MSOut7
Stop positioner when the light curtain is broken only if at side A or B.
  Reduces movement from using only switches
  Standstill not used during sweep because of Cat0 Stop. Servo off Cat1 used during sweep
S1 Final Standstill allows for custom content to be added

## Slide 32: DX200 ArcWorld IV 6X00 with integrated safety logic
S1 Standstill Positioner Trunion – MSOut7
Stop positioner when the light curtain is broken only if at side A or B.
  Reduces movement from using only switches
  Standstill not used during sweep because of Cat0 Stop. Servo off Cat1 used during sweep
S1 Final Standstill allows for custom content to be added

## Slide 33: DX200 ArcWorld IV 6X00 with integrated safety logic
S2/S3 Standstill SideA/B Tool – MSOut7&8
Stop tooling axis when at operator and light curtain broken.
  Eliminates need for tooling “in position” switches
  Allows for programmable load position
S2/S3 Final Standstill allows for custom content to be added

## Slide 34: DX200 ArcWorld IV 6X00 with integrated safety logic
S2/S3 Speed Limit SideA/B Tool – MSOut10&11
Speed limit tooling axis
  At operator side for joystick jog
    Due to safety distance issue
    30% speed was measured by standards via scope
S2/S3 Speed Limit allows for custom content to be added
All speed limit (standstill) FSU files are run when inputs are active.
  Standstill and speed limit will both function at the same time, thus restricting any motion.

## Slide 35: DX200 ArcWorld IV 6X00 with integrated safety logic
  FSU Files – Speed Limit

## Slide 36: DX200 ArcWorld IV 6X00 with integrated safety logic
  FSU Files – Speed Limit - Continued

## Slide 37: DX200 ArcWorld IV 6X00 with integrated safety logic
Servo Off Cat1
Stop robot(s) and positioner
  When light curtain is broken while positioner is sweeping
E-Stop & Gate circuits are still used in addition

## Slide 38: DX200 ArcWorld IV 6X00 with integrated safety logic
Side A/B Tooling power – MSOut11&12
Turns off when
  Programming Pendant E-Stop Pressed
  External E-Stop
  PB E-Stop. Standard continues to use, even though no box is present.
  Light curtain is invaded and tooling is at operator
    Risk assessment required for tooling control while light curtain invaded.
    Safety logic modifications required
  #1 FSB Out1&2 allows for custom content to be added

## Slide 39: DX200 ArcWorld IV 6X00 with integrated safety logic
Standard is verified by MFGF-266 check sheet.
  No change for safety PLC or integrated safety
Add additional documentation for checks required due to changes in system configuration/safety logic

## Slide 40: Program steps
  Review Standards located on the standard world jobs section of the inet. (AW6X00 & AW2X00)
  Write logic on paper in robot format
  Verify logic requirements for both E-Stop and safety. Only one servo off output. Use Cat1.
  Develope test plan for safety logic

## Slide 41: Program steps
  Enable Expansion Function
  Set I/O to Be used
    Machine safety and expansion function.
    Verify EDM status of machine safety
      Sync vs non sync.
    Functional safety
  Set SLC signal display setup
    Write/confirm
  Assign F safety output signals
    Write/confirm
  Assign SLC Ext output signals
    Write/confirm
  Enter logic – On Pendent at this time
    Enter a few lines at a time
    Write/Confirm
  I/O check
  Safety logic validation per test plan
  Backup files.

## Slide 42: Offline Logic Programming
MotoSimEG-VRC Version 2015 Sp2
  Supports inform software version 1.8
Software key required
Template file AW6X00integratedSaftey located on share point
Create YSFLogic.dat file to load into controllers
Decrease startup time
FAQ also located on share

## Slide 43: DX200 ArcWorld 2000 only integrated safety logic
New name for an old favorite (Fabworld)
Information located under Standard World Jobs
Theory of operation document explains safety operation, FSU files setup, and safety logic
Zone rings removed from robot(s)
  FSU Axis range monitoring replacement
Positioner in position switches removed
  Standstill speed limit replacement
Integrated safety logic uses status from FSU to solve logic and perform safety function.
  Reduces wiring and external hardware
FSU standard on R1 (and R2 AW2200)
SYS Critical FSU Funct Disabled alarm
Safety checkout of system uses QC check sheet

## Slide 44: ArcWorld 2000 only integrated safety logic
  Inputs for integrated safety logic
  #1 FSU In1 – Light Curtain Sta1 (hardwired)
  #1 FSU IN2 – Light Curtain Sta2 (hardwired)
  FSU files- Robot 1 and 2 zones

## Slide 45: DX200 ArcWorld IV 2000 only integrated safety logic
SLC Signal Display Setup
SLC EXT Signal Allocation

## Slide 46: DX200 ArcWorld IV 2000 only integrated safety logic

## Slide 47: DX200 ArcWorld 2000 only integrated safety logic
  Break down safety logic to specfic safety functions
  S1 Standstill – Stops motion of Station1 positioner
  S2 Standstill – Stops motion of Station2 positioner
  Servo Off Cat1 – Stops motion of robot and postioners
  FSU range limits

## Slide 48: DX200 ArcWorld 2000 only integrated safety logic
Homework
Review positioner Standstill logic
Review servo off logic
Review range monitoring zone(s), explain zone(s) limits

## Slide 49: Objectives
  Review Machine Safety Hardware
  Expansion function
  Response Time
  Safety Logic Circuit
  I/O configuration
  Offline Programming
  Standards applications